# Assignment 4
Rita fadlallah

Question 1
A wood frame wall that is built around 38mm x 90mm wood studs with a center-to-center distance of 400mm.The 90mm-wide cavity between the studs is filled with urethane rigid foam insulation. The inside is finish with 13-mm gypsum wallboard and the outside with 13-mm plywood and 13-mm x 200-mm wood bevel lapped siding. The insulated cavity constitutes 75% of the heat transmission area while the studs, plates, and sills constitute 21%. The headers constitute 4 % of the area, and they can be treated as studs.
# Find the 2 𝑅𝑅𝑈𝑈𝑛𝑛𝑖𝑖𝑡𝑡 values; determine the overall unit thermal resistance and the overall heat transfer coefficient.
Also, determine the rate of heat loss through the walls of a house whose perimeter is 50m and wall height is 2.5m in Las Vegas, Nevada, whose winter design temperature is -2 ˚C. Take the indoor design temperature to be 22 ˚C and assume 20% of the wall is occupied by glazing.

	WOOD	INSULATION
OUTSIDE AIR	0.03	0.03
WOOD BEVEL (13*20mm)	0.14	0.14
PLYWOOD (13mm)	0.11	0.11
URETHANE RIDGID FOAM INSULATION (90mm)	-	0.98*90/25= 3.5
WOOD STUDS (90mm)	0.63	-
GYPSUM BOARD (13mm)	0.079	0.079
INSIDE SURFACE	0.12	0.12
TOTAL m2.C/W	1.11	3.98

Rʹwith wood = (0.03 + 0.14 + 0.11 + 0.63 + 0.079 + 0.12) m2.C/W = 1.109 m2.C/W

Rʹwith insulation = (0.03 + 0.14 + 0.11 + 3.5 + 0.079 + 0.12) m2.C/W = 4.007 m2.C/W

Uwood

U
=	1
Rʹ𝑤𝑖𝑡ℎ 𝑤𝑜𝑜𝑑

=	1
=	1
1.109 m2.C/W

=	1
= 0.9017 m2.C/W

= 0.2496 m2.C/W
insulation
Rʹ𝑤𝑖𝑡ℎ 𝑤𝑜𝑜𝑑

4.007 m2.C/W

1	=	1	+	1
, R = 𝑅ʹ ; i.e. , 1
= 𝐴
Rʹ𝑡𝑜𝑡𝑎𝑙
Rˈ𝑤𝑜𝑜𝑑
R𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛	𝐴
R	Rʹ
𝐴𝑡𝑜𝑡𝑎𝑙

𝑅ʹ𝑡𝑜𝑡𝑎𝑙
= 𝐴𝑤𝑜𝑜𝑑
𝑅ʹ𝑤𝑜𝑜𝑑
+ 𝐴𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛
𝑅ʹ𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛
U= 1
𝑅ʹ
i.e. , Atotal * Utotal = Awood * Uwood + Ainsulation * Uinsulation

Utotal

= Uwood
* 𝐴𝑤𝑜𝑜𝑑
𝐴𝑡𝑜𝑡𝑎𝑙
+ Uinsulation
* 𝐴𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛
𝐴𝑡𝑜𝑡𝑎𝑙
= (21% + 4%) * Uwood + 75% * Uinsulation
= 25% * 0.9017 m2.C/W + 75% * 0.2496 m2.C/W

= 0.4126 m2.C/W

Overall thermal resistance R

value
=	1
𝑈𝑡𝑜𝑡𝑎𝑙
=	1
0.4126
m2. C/W = 2.4237 m2.C/W

Rate of heat loss through walls Qtotal = Utotal * Atotal *∆T

= 0.4126 m2.C/W * 50m * 2.5m *(1-20%) * 22 – (-2 ˚C) = 990.24W
Question 2
In 2 pages, write a summary about radiation and radiative heat transfer.

Thermal radiation is one of three mechanisms which enables bodies with varying temperatures to exchange energy. Thermal radiation is characterized by the emission of electromagnetic waves from the material (variation of its internal energy). Depending on the temperature of the material, it transmits radiation ranging from ultraviolet to far-field infrared. The entire body acts as an emission sourceof continuous thermal radiation, and also as a continuous receiver of radiation originating even from far-field bodies. However, thermal radiation is linked to the molecular structure of the transmitter, receiver, and the crossed medium. Surface radiation of a body is also linked to its capacity to transmit and store heat (specific temperatures). Further information on this can be found in specialized literature
Heat transfer from a body with a high temperature to a body with a lower temperature, when bodies are not in direct physical contact with each other or when they are separated in space, is called heat radiation , as schematically . All physical substances in solid, liquid, or gaseous states can emit energy via a process of electromagnetic radiation because of vibrational and rotational movement of their molecules and atoms . The intensity of such energy flux depends upon the temperature of the body and the nature of its surface . The radiation occurs at all temperatures, with the rate of emission increasing with the temperature.

Unlike conduction and convection, heat transfer by thermal radiation does not necessarily need a material medium for the energy transfer. In the case of thermal radiation from a solid surface, the medium through which the radiation passes could be vacuum, gas, or liquid. Molecules and atoms of the medium can absorb, reflect, or transmit the radiation energy. If the medium is a vacuum, since there are no molecules or atoms, the radiation energy is not attenuated and, therefore, fully transmitted. Therefore, radiation heat transfer is more efficient in a vacuum. In the case of a gas (e.g., air), energy can be slightly absorbed or reflected by air molecules and the balance is transmitted. For liquid medium, most of the radiation is absorbed is a thin layer close to the solid surface and nothing is transmitted