# Assignment 4
Hana Abou Baker

Question 1
A wood frame wall that is built around 38mm x 90mm wood studs with a center-to-center distance of 400mm.The 90mm-wide cavity between the studs is filled with urethane rigid foam insulation. The inside is finish with 13-mm gypsum wallboard and the outside with 13-mm plywood and 13-mm x 200-mm wood bevel lapped siding. The insulated cavity constitutes 75% of the heat transmission area while the studs, plates, and sills constitute 21%. The headers constitute 4 % of the area, and they can be treated as studs.
# Find the 2 𝑅𝑅𝑈𝑈𝑛𝑛𝑖𝑖𝑡𝑡 values; determine the overall unit thermal resistance and the overall heat transfer coefficient.
Also, determine the rate of heat loss through the walls of a house whose perimeter is 50m and wall height is 2.5m in Las Vegas, Nevada, whose winter design temperature is -2 ˚C. Take the indoor design temperature to be 22 ˚C and assume 20% of the wall is occupied by glazing.

	WOOD	INSULATION
OUTSIDE AIR	0.03	0.03
WOOD BEVEL (13*20mm)	0.14	0.14
PLYWOOD (13mm)	0.11	0.11
URETHANE RIDGID FOAM INSULATION (90mm)	-	0.98*90/25= 3.5
WOOD STUDS (90mm)	0.63	-
GYPSUM BOARD (13mm)	0.079	0.079
INSIDE SURFACE	0.12	0.12
TOTAL m2.C/W	1.11	3.98

Rʹwith wood = (0.03 + 0.14 + 0.11 + 0.63 + 0.079 + 0.12) m2.C/W = 1.109 m2.C/W

Rʹwith insulation = (0.03 + 0.14 + 0.11 + 3.5 + 0.079 + 0.12) m2.C/W = 4.007 m2.C/W

Uwood

U
=	1
Rʹ𝑤𝑖𝑡ℎ 𝑤𝑜𝑜𝑑

=	1
=	1
1.109 m2.C/W

=	1
= 0.9017 m2.C/W

= 0.2496 m2.C/W
insulation
Rʹ𝑤𝑖𝑡ℎ 𝑤𝑜𝑜𝑑

4.007 m2.C/W

1	=	1	+	1
, R = 𝑅ʹ ; i.e. , 1
= 𝐴
Rʹ𝑡𝑜𝑡𝑎𝑙
Rˈ𝑤𝑜𝑜𝑑
R𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛	𝐴
R	Rʹ
𝐴𝑡𝑜𝑡𝑎𝑙

𝑅ʹ𝑡𝑜𝑡𝑎𝑙
= 𝐴𝑤𝑜𝑜𝑑
𝑅ʹ𝑤𝑜𝑜𝑑
+ 𝐴𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛
𝑅ʹ𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛
U= 1
𝑅ʹ
i.e. , Atotal * Utotal = Awood * Uwood + Ainsulation * Uinsulation

Utotal

= Uwood
* 𝐴𝑤𝑜𝑜𝑑
𝐴𝑡𝑜𝑡𝑎𝑙
+ Uinsulation
* 𝐴𝑖𝑛𝑠𝑢𝑙𝑎𝑡𝑖𝑜𝑛
𝐴𝑡𝑜𝑡𝑎𝑙
= (21% + 4%) * Uwood + 75% * Uinsulation
= 25% * 0.9017 m2.C/W + 75% * 0.2496 m2.C/W

= 0.4126 m2.C/W

Overall thermal resistance R

value
=	1
𝑈𝑡𝑜𝑡𝑎𝑙
=	1
0.4126
m2. C/W = 2.4237 m2.C/W

Rate of heat loss through walls Qtotal = Utotal * Atotal *∆T

= 0.4126 m2.C/W * 50m * 2.5m *(1-20%) * 22 – (-2 ˚C) = 990.24W

Question 2
In 2 pages, write a summary about radiation and radiative heat transfer.

Thermal radiation, process by which energy, in the form of electromagnetic radiation, is emitted by a heated surface in all directions and travels directly to its point of absorption at the speed of light; thermal radiation does not require an intervening medium to carry it.

Radiation is a method of heat transfer that does not rely upon any contact between the heat source and the heated object. For example, we feel heat from the sun even though we are not touching it. Heat can be transmitted though empty space by thermal radiation. Thermal radiation (often called infrared radiation) is a type electromagnetic radiation (or light). Radiation is a form of energy transport consisting of electromagnetic waves traveling at the speed of light. No mass is exchanged and no medium is required.

Radiation is the system of emitting energy in the form of waves or particles through a medium or space. Sunshine is one of radiation's most acquainted forms. It offers warmness and light.
Radiation includes particles and waves of electromagnetic electricity emitted by using some materials.
Ionizing radiation has sufficient vitality to ionize (expel an electron from a particle) which can change the chemical composition of the fabric. Non-ionizing radiation has less vitality but can still energize atoms and particles causing them to vibrate quicker.

Not at all like conduction and convection, warm exchange by warm radiation does not essentially require a fabric medium for the vitality exchange. Within the case of warm radiation from a strong surface, the medium through which the radiation passes may well be vacuum, gas, or fluid. Atoms and particles of the medium can absorb, reflect, or transmit the radiation vitality. On the off chance that the medium could be a vacuum, since there are no atoms or particles, the radiation energy isn't weakened and, so, completely transmitted. In this manner, radiation warm exchange is more proficient in a vacuum. Within the case of a gas (e.g., discuss), vitality can be marginally retained or reflected by discuss atoms and the adjust is transmitted. For fluid medium, most of the radiation is ingested could be a lean layer near to the strong surface and nothing is transmitted.

Electromagnetic radiation can be considered as a wave of electric and attractive vitality travelling through a vacuum or a fabric. The electromagnetic range incorporates radio waves, microwaves, infrared beams, light beams, UV beams, X‑rays and gamma beams. All electromagnetic radiation is transmitted through purge space at the speed of light.
These properties moreover decide their capacity to travel through objects, their warming impacts and their impact on living tissue. Electromagnetic radiation is made when an nuclear molecule, such as an electron, is quickened by an electric field, causing it to move. The development produces oscillating electric and attractive areas, which travel at right points to each other in a bundle of light vitality called a photon.